## Slide 1
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
SMART INTELLIGENT CANE — EXECUTIVE SYSTEM ARCHITECTURE
Interactive Architecture: Click any of the 4 core architecture blocks below to drill down into its detailed Tree Structure
⚡ 50ms Deterministic Safety Loop | 📷 Dual AI Cameras (Top + Ground) | 🌡️ Dual Spatial PIRs | 🎧 Bluetooth Ear Assistant | 🔋 36h Battery Runtime
BLOCK 1 • 8 SENSORS • DUAL-TIER
Multi-Modal Perception & Sensing Layer
Full-body 360° environmental awareness from head height to pavement level:
• Top Forward Camera (OV5647 CSI-2)
• Bottom Ground Camera (120° USB UVC)
• Ultrasonic Sensor (40kHz JSN-SR04T)
• Laser ToF Step Sensor (VL53L1X)
• Dual Spatial PIRs (Torso + Blind Spot)
• BMI270 6-DOF IMU + Water Contact Pins
CLICK TO EXPAND TREE ➔
BLOCK 2 • RTOS + LINUX EDGE AI
Dual-Processor Brain & Safety Core
Asymmetric computing separating hard safety reflex from computer vision:
• ESP32-S3 Safety Core (Always-On)
• 50ms Deterministic FreeRTOS Loop
• Zero-Lag Hazard Priority Arbitration
• Raspberry Pi Zero 2 W (Switchable)
• YOLO-Fastest & MobileNet Vision AI
• Whisper.tflite Voice AI + 921k UART
CLICK TO EXPAND TREE ➔
BLOCK 3 • EARS-FREE AUDIO + HAPTICS
Assistive Output, HMI & Actuation Layer
Multi-channel sensory feedback leaving ears open for environmental hearing:
• Bluetooth 5.x Bone-Conduction Ear Link
• Top Apex Voice Mic (Mouth Aligned)
• DRV2605L Haptic Palm Reflex (<15ms)
• 4x Tactile Braille Buttons (V, E, I, P)
• Guarded Recessed Emergency SOS
• Quad-Pod Motorized Adaptive Tip
CLICK TO EXPAND TREE ➔
BLOCK 4 • 5 RAILS • STANDALONE SOS
Power Distribution, Cellular & Cloud
Fail-safe energy management and direct cellular emergency dispatch:
• 1S2P 6800 mAh Li-Ion Battery Pack
• 5 Isolated Switched Regulated Rails
• 36+ Hours Runtime in Power-Save
• SIM7600G-H LTE Cat-4 & GNSS Module
• Autonomous Direct-AT SOS (No Pi needed)
• Caregiver IoT Telemetry & Geo-Fencing
CLICK TO EXPAND TREE ➔
Tip: In PowerPoint Slide Show Mode (F5), clicking any block acts as an interactive button that opens that subsystem's full tree architecture.

## Slide 2
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
MULTI-MODAL PERCEPTION & SENSING SUBSYSTEM TREE
Detailed Tree: 8 Multi-Modal Sensors with Buses, Voltages, Rates, and Fail-Safe Paths
⬅ BACK TO 4-BLOCK OVERVIEW
ROOT ARCHITECTURAL BLOCK: MULTI-MODAL PERCEPTION & SENSING
Hierarchical Tree: Subsystems ➔ Dedicated Hardware Modules ➔ Software Drivers & Protocols
1. Optical Vision Suite
Dual-Camera Semantic Vision
Top Forward Camera (CAM1)
Part: OmniVision OV5647 (5MP) • Bus: 22-pin CSI-2 to RPi
Power: 5V_PI (250mA) • Rate: 30 fps @ 1080p
Scene comprehension, sign text OCR, crosswalks & pedestrian detection.
Bottom Pavement Camera (CAM2)
Part: Wide 120° Mini CMOS • Bus: USB UVC / CSI Mux
Power: 5V_PI (190mA) • Rate: 30 fps ground flow
Angled 35° down: Real-time curb, stair, pothole & drop-off segmentation.
Optical Vision AI Pipeline
Part: YOLO-Fastest + MobileNet • Bus: V4L2 Pipeline (Linux)
Power: Included in Pi • Rate: 15 fps quantized
Fused visual inference delivering obstacle tokens to audio guidance engine.
2. Acoustic & Laser Ranging
Zero-Lag Reflex Safety Path
Ultrasonic Sensor (SEN1)
Part: Waterproof JSN-SR04T (40kHz) • Bus: GPIO Trigger/Echo (ESP32)
Power: 5V_AUX (15mA) • Rate: 20 Hz (50ms cycle)
Acoustic distance ranging (20-450cm); triggers palm haptics directly.
Laser ToF Step Sensor (SEN2)
Part: ST VL53L1X (940nm VCSEL) • Bus: Diff I2C (PCA9615 buffer)
Power: 3V3_MAIN (16mA) • Rate: 50 Hz (20ms)
Millimeter pavement distance profiling; detects curbs & >8cm drop-offs.
Liquid Water Contact Pins (SEN5)
Part: Gold Electrode Contact Pins • Bus: Analog ADC (ESP32-S3)
Power: 3V3_MAIN (<10µA) • Rate: Polled every 50ms
Conductivity drop alerts user to standing water puddles before stepping.
3. Spatial Thermal Motion
Pedestrian & Blind-Spot Guard
Upper Spatial PIR (SEN3)
Part: Panasonic PaPIRs (120° FOV) • Bus: Hardware INT (ESP32-S3)
Power: 3V3_MAIN (<50µA) • Rate: Asynchronous IRQ
Mounted at torso height; detects approaching pedestrians & cyclists 4m away.
Lower Peripheral PIR (SEN4)
Part: Dual-Element Miniature PIR • Bus: TCA9555 Expander INT
Power: 3V3_MAIN (<50µA) • Rate: Asynchronous IRQ
Low-angle blind spot detection for moving pets, children, and scooters.
PIR Thermal Filter Engine
Part: ESP32 Firmware Interrupt ISR • Bus: FreeRTOS Event Group
Power: N/A (Firmware) • Rate: <1ms wake latency
Differentiates moving human heat signatures from ambient temperature drift.
4. Inertial & Vitals Tracking
Fall Detection & User Health
6-DOF IMU Sensor (U4)
Part: Bosch BMI270 (Ultra-low noise) • Bus: Diff I2C (Addr 0x68)
Power: 3V3_MAIN (680µA) • Rate: 100 Hz continuous
Freefall detection, impact spike trigger, gait cadence & terrain vibration FFT.
MAX30102 PPG Optical Vitals (U5)
Part: Maxim MAX30102 Heart/SpO2 • Bus: Handle I2C (Addr 0x57)
Power: 3V3_MAIN (600µA) • Rate: 25 Hz PPG
Monitors palm pulse and blood oxygen; validates consciousness post-fall.
Cadence & Freefall Algorithm
Part: Firmware Core 0 Classifier • Bus: FreeRTOS Safety Loop
Power: N/A (Firmware) • Rate: 10ms evaluation
Dual-threshold fall detection: freefall + high-G impact + 5s immobility.

## Slide 3
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
DUAL-PROCESSOR BRAIN & REAL-TIME SAFETY TREE
Detailed Tree: ESP32-S3 Hard RTOS & Raspberry Pi Zero 2 W Edge AI Architecture
⬅ BACK TO 4-BLOCK OVERVIEW
ROOT ARCHITECTURAL BLOCK: DUAL-PROCESSOR BRAIN & COMPUTE
Hierarchical Tree: Subsystems ➔ Dedicated Hardware Modules ➔ Software Drivers & Protocols
1. ESP32-S3 Safety Core (HW)
Always-On Hard Safety Master
ESP32-S3-WROOM-1 (U1)
Part: Dual Xtensa LX7 @ 240MHz • Bus: I2C, 2x I2S, 3x UART, ADC
Power: 3V3_MAIN (Always-On) • Rate: 240 MHz clock
Hardware root of trust; owns all safety sensors, haptics, and autonomous SOS.
TCA9555 16-Bit Expander (U7)
Part: TI TCA9555 I2C Expander • Bus: I2C (Addr 0x20) + INT
Power: 3V3_MAIN (5µA) • Rate: 100 kHz I2C
Gates power switches for Pi, cameras, and modem to enforce power saving.
PCA9615 Differential Buffer
Part: NXP PCA9615 I2C Buffer • Bus: Differential dI2C Pair
Power: 3V3_MAIN (12mA) • Rate: 400 kHz over 1.2m
Guarantees noise-immune I2C communication along cane shaft to tip sensors.
2. FreeRTOS Safety Firmware
Deterministic 50ms Real-Time Loop
50ms Deterministic Safety Loop
Part: FreeRTOS Real-Time Scheduler • Bus: Core 0 Task (Priority 10)
Power: N/A (Firmware) • Rate: Strict 50.0ms cycle
Executes 5 synchronized safety evaluations: Fall > Drop-off > Obstacle > Water.
DRV2605L Haptic Engine Driver
Part: I2C Waveform Synthesizer • Bus: Handle I2C (Addr 0x5A)
Power: 3V3_MAIN • Rate: <15ms trigger latency
Synthesizes distinct vibrotactile waveforms directly into user's palm.
Autonomous Direct-AT Modem Link
Part: UART AT Command Sequencer • Bus: UART1 to SIM7600G
Power: N/A (Firmware) • Rate: 115,200 baud direct
Dispatches emergency SMS and 112 call autonomously without Raspberry Pi.
3. Raspberry Pi Zero 2 W (HW)
Switchable Edge AI Gateway
Raspberry Pi Zero 2 W (U2)
Part: Broadcom BCM2710A1 • Bus: CSI-2, USB OTG, UART, BLE
Power: 5V_PI (Switched rail) • Rate: Quad 1.0 GHz Cortex-A53
Runs computer vision models, Whisper voice engine, and Bluetooth ear link.
Bluetooth 5.x BLE Transceiver
Part: Dedicated Audio Module • Bus: UART / PCM Audio Link
Power: 3V3_MAIN / 5V_PI • Rate: 2.4 GHz A2DP / LE Audio
Streams spoken guidance and obstacle tones to bone-conduction ear assistant.
Inter-Processor UART Bridge
Part: 4-Wire Framed Serial Protocol • Bus: Mini-UART + RTS/CTS + IRQ
Power: 3.3V Logic Level • Rate: 921,600 baud packetized
Bidirectional link exchanging obstacle tokens, voice chunks, and system health.
4. Edge AI Software Stack
Vision, Voice & Scene Engine
Dual-Camera Vision Inference
Part: YOLO-Fastest + MobileNet SSD • Bus: TFLite Int8 Engine
Power: N/A (Software) • Rate: 12-15 fps inference
Identifies obstacles, stairs, crosswalk signals, storefronts, and text OCR.
Whisper.tflite Voice Assistant
Part: Local Speech-to-Text Model • Bus: ALSA Audio Pipeline
Power: N/A (Software) • Rate: Triggered on 'V' hold
Transcribes user voice queries; pairs with cloud Gemini API for natural dialog.
Context & Caregiver Sync Engine
Part: MQTT Client + Local SQLite • Bus: SIM7600 USB Network Link
Power: N/A (Software) • Rate: 60s telemetry push
Maintains offline queue; syncs GPS tracks and incident logs to cloud.

## Slide 4
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
ASSISTIVE HMI, AUDIO GUIDANCE & ACTUATION TREE
Detailed Tree: Bone-Conduction Ear Assistant, Top Voice Mic, Palm Haptics & Adaptive Tip
⬅ BACK TO 4-BLOCK OVERVIEW
ROOT ARCHITECTURAL BLOCK: ASSISTIVE HMI & OUTPUT ACTUATION
Hierarchical Tree: Subsystems ➔ Dedicated Hardware Modules ➔ Software Drivers & Protocols
1. Audio Guidance & Ear Assistant
Ears-Free Wireless Navigation
Bluetooth Ear Assistant Transceiver
Part: Dedicated BT 5.x / LE Audio • Bus: UART/PCM to RPi Zero 2 W
Power: 3V3_MAIN (18mA streaming) • Rate: Sub-30ms audio latency
Guides user via bone-conduction headphones; keeps ears open for traffic.
Top Apex Voice Microphone (MIC1)
Part: Knowles SPH0645LM4H High-SNR • Bus: I2S Audio Bus (64x Fs)
Power: 3V3_MAIN (1.4mA active) • Rate: 16 kHz / 24-bit PCM
Acoustic port on top cap directed at mouth for crystal-clear voice AI commands.
Thumb-Arch Tri-Mic Array
Part: 3x Knowles MEMS Microphones • Bus: I2S0 (Stereo) + I2S1 to ESP32
Power: 3V3_MAIN (3.5mA total) • Rate: Spatial beamforming
Suppresses wind noise and detects approaching sirens or vehicle horns.
Handle Siren & Speaker Amp (U8)
Part: MAX98357A I2S Class-D Amp • Bus: I2S1 Bus (shared clocks)
Power: 5V_AUX (600mA loud siren) • Rate: Up to 92 dBA alarm
High-decibel audible emergency siren alerts passersby during a fall or distress.
2. Palm Haptics & Tactile Inputs
Sub-15ms Tactile Reflex Interface
DRV2605L Haptic Motor Driver
Part: TI DRV2605L + Grip LRA Motor • Bus: Handle I2C (Addr 0x5A)
Power: 3V3_MAIN (80mA pulse) • Rate: <15ms reflex trigger
Immediate palm vibration: Proximity ticks, curb double-pulse, and emergency buzz.
4x Tactile Braille Buttons
Part: Raised Braille Tactile Switches • Bus: Dedicated GPIOs (Active-Low)
Power: Internal Pull-Up • Rate: 10ms debounced IRQ
V (Voice AI), E (Environment summary), I (Incident tag), P (Power toggle).
Guarded Emergency SOS Button
Part: Recessed Switch with Guard Ring • Bus: ESP32 Deep Sleep Wake GPIO
Power: Pull-Up to 3V3_MAIN • Rate: 2-second hold required
Prevents accidental press; 2s hold triggers autonomous SMS/Call with GPS.
3. Mechanical Quad-Pod Stabilization
Motorized Adaptive Terrain Tip
Quad-Pod Tip Motor Driver
Part: TI DRV8830 I2C Motor Driver • Bus: Diff I2C (Addr 0x60)
Power: VBAT_MOTOR (Fused 3.7V) • Rate: 1.2s deployment time
Drives miniature DC gear-motor and lead screw collar to expand support legs.
3 Articulated Folding Support Legs
Part: CNC Aluminum Linkage Legs • Bus: Mechanical Lead Screw Hub
Power: N/A (Mechanical) • Rate: Full 4-point ground base
Deploys automatically on rough gravel or inclines; allows cane to self-stand.
Ergonomic Thumb-Arch Handle
Part: Overmolded Polycarbonate Chassis • Bus: Keyed 20-Pin Joint J1
Power: N/A (Mechanical) • Rate: Rated for 50 kg load
Optimized palm posture, integrated camera pod, and quick-release latch.

## Slide 5
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
POWER DISTRIBUTION, CELLULAR SOS & CLOUD TREE
Detailed Tree: 5 Switched Rails, 6800mAh Battery, SIM7600G Modem & IoT Cloud
⬅ BACK TO 4-BLOCK OVERVIEW
ROOT ARCHITECTURAL BLOCK: POWER DISTRIBUTION & CLOUD TELEMETRY
Hierarchical Tree: Subsystems ➔ Dedicated Hardware Modules ➔ Software Drivers & Protocols
1. Energy Storage & Charging
1S2P 6800 mAh Li-Ion Architecture
1S2P 6800 mAh Li-Ion Battery
Part: 2x Panasonic NCR18650GA • Bus: Direct Raw Cell (VSYS)
Power: 3.0V to 4.2V (24.5 Wh) • Rate: Up to 8A burst current
Single-cell parallel configuration eliminates cell balancing failure modes.
BQ25895 USB-C Fast Charger
Part: TI BQ25895 Switch-Mode Charger • Bus: USB-C CC1/CC2 PD Logic
Power: Up to 3.0A fast charge • Rate: 93% charging efficiency
Charges cane in <2.5 hours with thermal regulation and overvoltage protection.
BQ27441 Fuel Gauge IC
Part: TI BQ27441-G1 System-Side Gauge • Bus: I2C Bus (Addr 0x55)
Power: VSYS (<50µA draw) • Rate: 1 Hz state-of-charge
Provides accurate battery state-of-charge (%) to drive power-save transitions.
2. Five Isolated Switched Rails
Independent Rail Gating Architecture
3V3_MAIN Rail (Always-On)
Part: TPS63020 Buck-Boost Regulator • Bus: Powers ESP32, IMU, ToF, Mics
Power: 3.30V @ up to 2.0A • Rate: 96% efficiency
Seamless 3.3V regulation across full 3.0V-4.2V battery discharge curve.
5V_PI Rail (Switched)
Part: TPS61088 Boost + TPS22918 Switch • Bus: Powers Pi Zero 2 W & Cams
Power: 5.0V @ up to 2.5A • Rate: Switched by TCA9555 P00
Cleanly disabled in POWER_SAVE mode (<20% battery) to extend runtime to 36+ hrs.
5V_AUX Rail (Switched)
Part: TPS61088 Boost + TPS22918 Switch • Bus: Powers Ultrasonic & Audio Amp
Power: 5.0V @ up to 1.0A • Rate: Switched by TCA9555 P03
Stays active during POWER_SAVE mode so ultrasonic safety protection never stops.
VBAT_MODEM & VBAT_MOTOR
Part: Dedicated TPS22918 Load Switches • Bus: Direct VSYS with 1000µF cap
Power: Raw Cell (3.0V - 4.2V) • Rate: 2.0A peak RF bursts
Isolates noisy modem bursts and motor inrush from sensitive digital sensors.
3. Cellular SOS & Cloud IoT
Dual-Link Autonomous Emergency Link
SIM7600G-H LTE & GNSS Module
Part: Global LTE Cat-4 + Multi-GNSS • Bus: Dual: UART (ESP) + USB (Pi)
Power: VBAT_MODEM (2A bursts) • Rate: 150 Mbps DL / 50 Mbps UL
Dual-path cellular modem allowing autonomous SOS calls from ESP32-S3.
Autonomous Emergency SOS Dispatch
Part: Direct AT Command Firmware • Bus: ESP32-S3 UART1 to Modem
Power: Active in all modes • Rate: <5s dispatch latency
Sends emergency SMS with Google Maps pin & places 112 calls without needing Pi.
Caregiver IoT Cloud Dashboard
Part: MQTT TLS 1.3 / REST API • Bus: Cellular IP Socket (RPi)
Power: Cloud Infrastructure • Rate: 60s heartbeat telemetry
Caregiver portal: Real-time map location, fall incident history & geo-fence alerts.

## Slide 6
SMART INDIA HACKATHON 2026 • SYSTEM ARCHITECTURE
SMART INTELLIGENT CANE — MASTER SYSTEM ARCHITECTURE TREE
Complete Consolidated Tree: 4 Architectural Pillars, Subsystems, Hardware Components & Software Dataflows
⬅ BACK TO 4-BLOCK OVERVIEW
1. Multi-Modal Perception
Sensors & Drivers
Top Forward Camera (CAM1)
OV5647 5MP • CSI-2 (22-pin)
Bottom Ground Camera (CAM2)
120° Wide • USB UVC • Curbs/Stairs
Ultrasonic Rangefinder (SEN1)
JSN-SR04T 40kHz • 50ms Safety Loop
Laser ToF Step Sensor (SEN2)
ST VL53L1X • Diff I2C • Drop-offs
Upper Spatial PIR (SEN3)
Panasonic 120° • Pedestrian IRQ
Lower Blind-Spot PIR (SEN4)
Low-angle blind spot detection
6-DOF IMU Sensor (U4)
BMI270 100Hz • Freefall Spike
MAX30102 PPG + Water Pins
Heart Rate/SpO2 + Puddle Immersion
2. Dual-Processor Brain
RTOS Safety + Edge AI
ESP32-S3 Safety Core (U1)
Dual Xtensa 240MHz • Always-On
50ms FreeRTOS Safety Loop
Deterministic Priority Arbitration
DRV2605L Haptic Engine
Sub-15ms Palm Reflex Waveforms
TCA9555 Expander & Load Switch
Gates Rails for 36h Power-Save
Raspberry Pi Zero 2 W (U2)
Quad Cortex-A53 1.0 GHz • Switchable
Dual-Camera Vision Pipeline
YOLO-Fastest & MobileNet Int8
Whisper.tflite Voice Assistant
Local STT + Cloud Multimodal NLP
Inter-Processor UART Bridge
Framed 4-Wire Serial @ 921,600 baud
3. Assistive Output & HMI
Audio, Haptics & Legs
Bluetooth Ear Assistant (U3)
Dedicated BLE/A2DP Bone Conduction
Top Apex Voice Mic (MIC1)
Mouth-Aligned Acoustic Port
Thumb-Arch Tri-Mic Array
Spatial Beamforming & Sirens
DRV2605L Haptic Palm Motor
Linear Resonant Actuator (LRA)
Tactile Braille Buttons
V (Voice), E (Env), I (Inc), P (Pwr)
Guarded Emergency SOS Button
Recessed Switch • 2s Hold Dispatches
MAX98357A 92dBA Siren
Audible Siren for Falls & Distress
Quad-Pod Adaptive Tip
DRV8830 Motor + 3 Articulated Legs
4. Power, Cellular & Cloud
5 Rails & IoT Cloud
1S2P 6800 mAh Li-Ion Pack
2x 18650 Cells • USB-C Fast Charge
3V3_MAIN Buck-Boost Rail
TPS63020 Always-On • Full 3.0-4.2V
5V_PI Switched Boost Rail
TPS61088 Boost • Powers Pi/Cameras
5V_AUX Switched Boost Rail
Independent switch for Ultrasonic
SIM7600G-H LTE & GNSS
Multi-band 4G + GPS/GLONASS
Autonomous Direct-AT SOS
Dispatches SMS/Call without RPi
Caregiver IoT Cloud Portal
MQTT TLS 1.3 • Live GPS Tracking
4-Stage Power State Machine
Normal > Power-Save (36h) > SOS